## Slide 1: Electronic System Design ELC 4001
Prof. Serag E. D. Habib
” وما بكم من نعمة فمن الله “
Final Project
2024

## Slide 2
Project Objective
Design a Modular Array for Multiplication & Division
Features:
* Unsigned binary numbers
* Multiplier Mode : 5bit * 5 bit
* Divider Mode: 10 bit
* Objective: maximum speed

## Slide 3
Project Subject / Array Multiplier
Array Binary Multiplier Circuit

## Slide 4
Project Subject / Array Divider
Array Binary Division Circuit
Pencil and paper division:
Successive subtractions / additions
division algorithm includes decision boxes
Example – Restoring division algorithm: Divide 21 / 4
Quotient = 101 Remainder = 1

## Slide 5
Project Subject / Array Divider
Non-restoring division algorithm: Divide 21 / 4
Quotient = 101 Remainder = 1

## Slide 6
Project Subject / Array divider
Left shift & Right Shift array Multipliers

## Slide 7
Project Subject / Array Divider
Structure of non-restoring array divider
Note: D0 is the MSB of dividend

## Slide 8
CUSCLIB Standard cell Library
104 Standard cells developed by previous students of this course
0.5 µm Scalable Nwell CMOS process
Examples :
Cairo University Standard Cell Library (CUSCLIB):
Gate | description | W/L for NMOS Tr. | W/L for PMOS Tr.
NAND | 2 input Nand Gate | 1/1 | 1/1
NAND | 2 input Nand Gate | 1/1 | 2/1
NAND | 2 input Nand Gate | 1/1 | 3/1
Xor | 2 input Xor Gate | 1/1 | 1/1
AND-OR-INVERT | 2-Input AND into 2-Input NOR | 1/1 | 1/1
Majority | Majority (AB+AC+BC) | 1/1 | 3/1
Multiplexer | 2:1 multiplexer | 1/1 | 1/1
1 bit Comparator cell | Equality output | 1/1 | 1/1
ADDER | Half adder | 1/1 | 2/1
D-FF | Slave cell of static D FF |  | 
D-FF | Master cell of static D FF |  | 

## Slide 9
CUSCLIB Standard cell Library
i ) Cell height 40 λ
ii ) VDD runs on a 5λ strip of Metal 1 located at height 34.5 λ to 39.5 λ
iii ) GND runs on a 5λ strip of Metal 1 located at height 0.5 λ to 5.5 λ
iv ) Inputs and outputs of each cell are available via vertical Metal 2 wires
Each standard cell satisfies the following guidelines:

## Slide 10
IO cells and Pads
i ) Latch
ii ) level protection
Min. functionality required from digital I/P cell
Min. functionality required from Digital O/P cell
i ) Tri-state buffer
ii ) High current drive

## Slide 11
IO cells and Pads
Pad
I/O cell

## Slide 12
Full layout
Remember: I/O cells require VDD and Gnd power lines !!
Corner cell
VDD I/P cell and Pad
Gnd I/P cell and Pad
When IO cells are abutted, VDD and GND cells create power ring around the chip that supplies power to all IO cells

## Slide 13
Full layout